## Slide 1: DRD Solar Home Systems in Myanmar: Recommendations & points for discussion
NEP Workshop on Off-Grid Electrification in Myanmar
Grand Ball Room, Thingaha Hotel, Nay Pyi Taw
January 28-29, 2015
Chris Greacen

## Slide 2: Outline
Technical
  Improve DRD SHS design specifications (short term)
  Revise DRD SHS specs to include quality standards
Policy, planning & regulation
  Integrate NEP geospatial plan into village selection
  Integrate sources of funding
  SPP/Mini-grid Regulatory framework
Financing & subsidies
  Redesign DRD SHS program (BIG!)
Organizational process & intuitional capacity
  Training for DRD
  Training & certification for installers
  Training for users (DVD & booklet)
  Public exposure to quality products
  Product review app
Environmental and Social
  Battery recycling

## Slide 3: Technical
    Improve DRD SHS design specifications
  Activity: improve SHS system design, increasing reliability and efficiency through removing inverter, enabling reduction in PV, battery capacity
  Reason needed: Inverter is inefficient & failure-prone and not needed for lights, TV, cell phone charging, fan.
Qty | Item | Current DRD Specifications | Recommended Capacity
1 | Solar panel | 80-90 peak watts | 60 peak watts
1 | Deep cycle battery | 65 Ah | 60 Ah
1 | Charge Controller | 10 A | 10 A
1 | Tube lamp | 20 watts (cfl) | 8-10 watts (LED)
2 | LED lamps | 3 to 5 watts | 3 to 5 watts
1  0 | Inverter | 300 watts | None
 | Quality standards | None except warranty | Certified components, adequate wiring, proper installation, warranty
SHORT TERM MEASURE
Notes: This is a somewhat limited tweak… if one wants to continue with the existing one-size SHS program, this revision of system design would improve chances of sustainability.

## Slide 4: Technical
    Revise DRD SHS specifications to include quality standards
  Activity: Reform the DRD SHS specifications so that any SHS that receive DRD subsidies must use equipment that meets certain quality standards, and that the system is correctly installed.
  Reason needed: Current DRD specifications are insufficient to ensure quality
Example from 44-page list of approved type-tested equipment for IDCOL
Source: http://www.idcol.org/download/260275fd02d802e8ded266af02d51ea5.pdf
Notes: As I discussed in yesterday’s presentation on the status of SHS, there are significant quality problems with the SHS built under the existing DRD specifications. Subsidies can be used to leverage quality by requiring that to be eligible to receive a subsidy, the SHS has to use equipment that has passed quality tests, and that the equipment is installed correctly.
A good starting point for a list of quality products might be to ride the coat-tails of the IDCOL program which has tested hundreds of different components. Their list is available at the website shown. Shown here is one page from the charge controller section.
In the IDCOL program, households can choose to install SHS over a wide range of sizes, but components have been tested.

## Slide 5: Policy, planning & regulation
Integrate NEP geospatial plan into village selection
  Activity: Adjust DRD SHS village selection process to include consideration of National Electrification Plan.
    Share NEP geospatial planning documents with township level (and above) DRD staff
    Update NEP regularly
    Develop clear criterion for village or household eligibility, e.g. SHS for villages not expected to be served by the grid within three (five?) years.
  Reason needed: As NEP is only recently completed, it has no connection with the selection of villages in the DRD SHS program.
    Risk of repeated selection of villages that may be quickly connected to the main grid.

## Slide 6: Policy, planning & regulation
Integrate NEP geospatial plan into village selection
Source: Columbia Earth Institute, 2014. Electrification Planning for Myanmar: Methodology and Sample Results for: Kayin State and Chin State. March 19, Nay Pyi Taw, Myanmar

## Slide 7: Policy, planning & regulation
    Integrate sources of funding beyond DRD budget
  Activity: Develop an institution or a financial account within DRD that can pool multiple sources of funding earmarked for rural energy support.
    Example: Rural Energy Agencies (REAs) in several African countries
  Reason needed: Coordinated funding energy access necessary to avoid proliferation of projects and programs working at cross purposes, duplicating efforts in some areas and leaving gaps in others.

## Slide 8: Subsidy and finance
    Redesign DRD SHS program
  Activity: Consider redesign of DRD SHS program to reduce subsidy amount, increase customer choice, integrate with commercial sales of SHS, enhance sustainability.
  Reason needed: Improve efficiency of government budget use.
  Program redesign is a big undertaking…
  requires answers to difficult questions

## Slide 9: Policy, planning & regulation
    Redesign DRD SHS program (continued)
  Key questions include:
    Should there be user subsidies? If so to what amount?
      Bangladesh = Initially $90/SHS, now $20/SHS; Lighting Global type program no subsidy
    Subsidy for market development?
    Specification: Fixed capacity vs. service level, or none?
      Fixed capacity: e.g. 80 watt PV, 65 Ah battery
      Service level: e.g. 3@180 lumen lights 4 hrs/night
    Micro-financing?
  More information needed on willingness to pay, elasticity of demand with respect to price

## Slide 10: Organizational process and institutional capacity
Training for DRD
  Activity: targeted training to the DRD on SHS.
    Topics to include:
      SHS failure modes
      Quality certification
      Specific information on how quality equipment and installation can help mitigate failure modes.
      Designing and running a sustainable program
  Reason needed: DRD is responsible for off-grid electrification but its engineering strengths lie largely in civil and mechanical engineering.

## Slide 11: Organizational process and institutional capacity
Training and certification for installers
  Activity: a train-the-trainer course and accreditation procedure for institutions that teach a course of between 4 to 7 days on SHS
    Content would follow accepted established international curriculum for SHS installer certification
  Reason needed: All SHS visited in the course of this research had shortfalls that compromise safe and efficient performance.

## Slide 12: Organizational process and institutional capacity
Library of best-practice SHS videos for installers
  Activity: Create a library of Burmese language 3-10 minute videos of best SHS practices calibrated to the Myanmar context.
    Content would vary from operational and basic maintenance to more technical material related to system design and installation best-practice.
  Reason needed: Video format takes advantage of the fact that DVD players and smart phones are already common in rural areas, video is a medium easily copied, and combines audio/visual learning.

## Slide 13: Organizational process and institutional capacity
videos and booklet for SHS users
  Activity: Create a simple pictorial booklet and videos in Burmese for best SHS user practices, calibrated to the Myanmar context.
  Reason needed: Poor understanding by system users of SHS installation, operation, and maintenance severely compromises system performance.

## Slide 14: Organizational process and institutional capacity
Burmese smartphone SHS product review app
  Activity: Create and market a Burmese-language smart-phone app for solar product review and discussion.
  Reason needed: Consumers have little information at their disposal to make purchase decisions on solar equipment.

## Slide 15: Organizational process and institutional capacity
    Public exposure to quality products
  Activity #1: Convene or facilitate exhibitions in which manufacturers can showcase quality equipment;
  Activity #2: Use multiple media channels to provide information on products that pass quality standards. Recommend draw from:
    IDCOL’s list of approved SHS components; and
      www.idcol.org/download/260275fd02d802e8ded266af02d51ea5.pdf
    Global Lighting’s website of products that have met Lighting Global Quality Standards.
      www.lightingglobal.org/products/?view=grid
  Reason needed: Widespread use of reliable, affordable SHS will be more achievable if the general public has information about the best products available.

## Slide 16: Environmental and Social
Battery recycling
  Activity: Investigate existing lead acid recycling practices and whether existing recyclers can scale up to match demand as SHS usage grows. Design & implement battery collection and recycling program if necessary.
  Reason needed: Lead is a potent neurotoxin and it is important to ensure that discarded SHS batteries do not pollute the environment. Sulfuric acid from batteries is also a hazard.

## Slide 17: Summary
Area | Activity | Timeframe
Policy, planning & regulation | Integrate NEP geospatial plan into village selection | 1 year
 | Integrate sources of funding | 1 year
Technical | Revise DRD SHS specs to include quality standards | 6 months
 | Improve DRD SHS design specifications | 2 months
Financing & subsidies | Redesign DRD SHS program (BIG!) | 1-2 years
Organizational process & intuitional capacity | Training for DRD | 3 months
 | Training & certification for installers | 6 months to 1 year
 | Training for users | 1 year
 | Public exposure to quality products | 6 months
 | Product review app | 6 months
Environmental and Social | Battery recycling | 1-2 years

## Slide 18: Thank you!
Chris Greacen
chrisgreacen@gmail.com